## Slide 1: CSE - 313 Computer Architecture
Faculty: Shoib Ahmed Shourav
United International University

## Slide 2: Memory Organization

## Slide 3: Components
Datapath
Memory
Processor
Input
Output
Control
Datapath
Processor
Input
Output
Control

## Slide 4: Reality!
Memory is the required for storing
  Program
  Data
Programmers want unlimited amounts of memory with low latency
Different memory types
  Static RAMs
  Dynamic RAMs
  Magnetic disk
How to make memory Bigger, Faster, and Cheaper?

## Slide 5: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables(Fixed inc/dec)
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data

## Slide 6: How does hardware exploit principle of locality?
Organize memory system into a hierarchy
  Multiple levels of memory with different speeds and sizes
  Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor

## Slide 7: How does hardware exploit principle of locality
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory

## Slide 8: Memory Hierarchy

## Slide 9: Memory Hierarchy: Terminology
Block (or line)
  The minimum unit of information that can be either present or not present in the memory
If accessed data is present in upper level
  Hit: access satisfied by upper level
If accessed data is absent in upper level
  Miss: block copied from lower level

## Slide 10: Memory Hierarchy: Terminology
Hit: data appears in some block in the upper level
  Hit Rate/Hit Ratio: hits/accesses, i.e., the fraction of memory access found in the upper level
  Hit Time: Time to access the upper level which consists of
  Access time + Time to determine hit/miss
Miss: data needs to retrieve from a block in the lower level
  Miss Rate/ Miss Ratio = misses/accesses = 1 - (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level + Time to deliver the block to the processor
Hit Time << Miss Penalty

## Slide 11: Cache
Cache memory
  The level of the memory hierarchy closest to the CPU based on SRAM
  Memorize the most frequently accessed DRAM memory locations to avoid repeatedly paying for the DRAM access latency
Cache
Processor
Main
Memory
Address
Address
Data
Data

## Slide 12: Cache
Which information goes into the cache?
  Access to word Xn
  Create a miss
  Load Xn into the cache

## Slide 13: Cache
How do we know if the data is present?
Where do we look?
Simple approach: Direct mapping
  Every memory location can be mapped only to exactly one cache position
Mapping:
  (Block address) modulo (number of cache blocks in the cache)

## Slide 14: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)

## Slide 15: Tags and Valid Bits
Difference?
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 16: Direct Mapped Cache Example
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Block offset
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator

## Slide 17: Cache: Read Algorithm

## Slide 18: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
Cache 8-blocks,Ram 32-Blocks, 1 word/block, direct mapped
Initial state

## Slide 19: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 20: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 21: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 22: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 23: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | ? | 010

## Slide 24: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 25: Multiword Block Direct Mapped Cache
Four words/block, cache size = 1K words
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
Notes: to take advantage for spatial

## Slide 26: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
  More competition  increased miss rate
Larger miss penalty
  Can override benefit of reduced miss rate

## Slide 27: Cache Size
32-bit byte address
A direct-mapped cache
The cache size is 2n blocks
The block size is 2m words (2m+2 bytes)
What is the size of the tag field?
  32-(n+m+2)
n select cache block
m select words within block
2 select byte within word

## Slide 28: Cache Size
32-bit byte address
A direct-mapped cache
The cache size is 2n blocks
The block size is 2m words (2m+2 bytes)
What is the size of the cache (unit: no. of bit)?
  2n X (2m X 32 + 32-(n+m+2) +1)

## Slide 29: Mapping an Address to a Multiword Cache Block
64 blocks, 16 bytes/block
To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits

## Slide 30: Cache Example
32-bit byte address
A direct-mapped cache
What is the cache line size (in words)?
4
How many entries does the cache have?
64
Tag | Index | Offset
31-10 | 9-4 | 3-0

## Slide 31: Problem-1
Suppose you are required to design a 512 KB cache with 4 words data per block. Each word contains 4 bytes of data. There are 32 bits the memory address.
(a) Calculate the number of blocks in the cache
(b) Find out the number of index bits and tag bits
(c) Calculate the actual size of the cache
512 KB / 4 Words
(2^9 * 2^10)/ (2^2 * 2^2)=2^19/ 2^4 = 2^15=2^n
m = 2 & n(index)=15
Tag= 32-(n+m+2) = 32- (15+2+2)= 32-19= 13
1KB=1024B

## Slide 32
a)
  (512*2^10)/4*4=B) 2^15
  Index(n)=15
  Offset=(word)2+(byte)2=4
  Tag= 32-(15+4)=13
c)
2^15*(1(valid bit)+13+4*4*8)

## Slide 33: Problem-2
Suppose you have designed a 256 KB cache with 2 words data per block.
(a) Calculate the miss rate for the following memory address accesses. Memory is byte ad-dressable.
12, 42, 7, 15, 40, 39
(b) Suppose you have changed the cache design to 4 words data per block. Calculate the miss rate in this case for the scenario in part (a).
(c) Explain the principle of locality that caused the change in miss rate in (b)

## Slide 34
# of blocks = (2^8*2^10)/(2*2^2)=2^15
12 :
  Block address= Floor(12/8)=1 [Type of hashing]
  Block number = Block address % # of blocks = 1% 2^15 =1
  [note : 8-15 complete address copied]
  Result : Miss
42:
  Block address= Floor(42/8)=5
  Block number = Block address % # of blocks = 5% 2^15 =5
  [note : 40-47 complete address copied]
  Result : Miss

## Slide 35
7 : miss [0-7]
15 : hit
40 : hit
39 : miss [32-39]
Miss rate : 4/6 = (4/6)*100 %

## Slide 36: Cache Example
32-bit byte address
A direct-mapped cache
What is the hit ratio?
0.25

## Slide 37: Handling Cache Misses
Read misses
  Stall execution, fetch the block from the next level in the memory hierarchy, install it in the cache, send requested word to processor, and then let execution resume
Write misses
  Write allocate: Stall execution, fetch the block from next level in the memory hierarchy, install it in cache, write the word from processor to cache, also update memory, then let execution resume
  or
  No-write allocate: skip the cache write and just write the word to memory

## Slide 38: Cache-Memory Consistency? (1/2)
Need to make sure cache and memory have same values on writes: 2 policies
1) Write-Through Policy: write cache and write through the cache to memory
  Every write eventually gets to memory
  Too slow, so include Write Buffer to allow processor to continue once data in Buffer, Buffer updates memory in parallel to processor

## Slide 39: Cache-Memory Consistency? (2/2)
Need to make sure cache and memory have same values on writes: 2 policies
2) Write-Back Policy: write only to cache and then write cache block back to memory when evict block from cache
  Writes collected in cache, only single write to memory per block
  Include bit to see if wrote to block or not, and then only write back if bit is set
    Called “Dirty” bit (writing makes it “dirty”)

## Slide 40: Write Through vs. Write Back
Advantages
  Write through
    Misses are simpler and cheaper because they never require a block to be written back in the lower level
    Easier to implement
  Write Back
    Individual words can be written by the processor at the rate that the cache, rather than the memory, can accept them
    Multiple writes within a block require only one write to the lower level in the hierarchy
    When blocks are written back, the system can make effective use of a high bandwidth transfer, since the entire block is written

## Slide 41: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
  CPU time = (CPU execution clock cycles + Memory-stall clock cycles) X Clock cycle time
  Memory-stall cycles = memory accesses/program × miss rate × miss penalty

## Slide 42: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss cycles per instruction = Miss rate * Miss penalty
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster!

## Slide 43: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 44: Any Question?
?