## Slide 1: CSE - 313 Computer Architecture
Faculty: Shoib Ahmed Shourav
United International University

## Slide 3: MIPS Assembly Language
MIPS memory
  Programming languages have simple variables that contain single data elements as in these examples, but they also have more complex data structures—arrays.
Word by word
Data transfer instructions
  lw(load word)
  sw(store word)
Size of the MIPS memory?

## Slide 4: MIPS Assembly Language
What is spilling registers?
  The process of putting less commonly used variables (or those needed later) into memory is called spilling registers.

## Slide 5: MIPS Assembly Language
Array:
  Assume variable h is associated with register $s2 and the base address of the array A is in $s3. What is the MIPS assembly code for the C assignment statement below?

## Slide 6: MIPS Assembly Language
Try following C codes:
  h = 230;
  A[10] = h + B[i];
  Suppose, Compiler will assign A (base address) into $s0, B(base address) into $s1, h into $s2 and i into $s3.
  addi $s2,$zero, 230

## Slide 7: MIPS Assembly Language
Instructions for making Decisions:
  beq $x, $y, Label(Memory address)
    If $x == $y then jump to the specified Label or address
    Otherwise go next
  bne $x, $y, Label(Memory address)
    If $x != $y then jump to the specified Label or address
    Otherwise go next
  slt $t, $x, $y
    If $x < $y then set 1 at $t, otherwise 0
  slti $t, $x, constant

## Slide 8: MIPS Assembly Language
beq, bne are conditional jump
There are some other instructions that are unconditional jump
  j memory_address/Label
  jal memory_address/Label
  jr $ra

## Slide 9: MIPS Assembly Language
Example:
  if (i == j) f = g + h;
  else f = g –h;
Let, compiler will assign f at $s0, g at $s1, h at $s2, i at $s3 and j at $s4
Solution:
  PC1000: beq $s3, $s4, IF // PC1000binary(32bits)
  1004: sub $s0, $s1, $s2 // PC= PC+4 ; PC= New JA
  1008: j EXIT
  1012: IF: add $s0, $s1, $s2
  1016: EXIT:

## Slide 10: MIPS Assembly Language
Example:
  if (i < j) f = g + h;
  else f = g –h;
Let, compiler will assign f at $s0, g at $s1, h at $s2, i at $s3 and j at $s4
Solution:
  slt $t0, $s3, $s4
  beq $to, $zero, Else
  add $s0, $s1, $s2
  j Exit
  Else: sub $s0, $s1, $s2
  Exit:

## Slide 11: MIPS Assembly Language
Example:
  if (i <= j) f = g + h;
  else f = g –h;
Let, compiler will assign f at $s0, g at $s1, h at $s2, i at $s3 and j at $s4
Solution:
  slt $t0, $s3, $s4
  beq $to, $zero, IF
  L1: add $s0, $s1, $s2
  j Exit
  IF: beq $s3, $s4, L1
  sub $s0, $s1, $s2
  Exit:

## Slide 12: MIPS Assembly Language
Try this one:
  if (i < j && i != k) f = g + h;
  else f = g –h;
Let, compiler will assign f at $s0,g at $s1,h at $s2,i at $s3,j at $s4 and k at $s5

## Slide 13: MIPS Assembly Language
Loop:
Example:
  while(save[5] == k) i++;
Let, compiler will assign I at $s0,k at $s1 and save at $s2
Solution:
  Loop:
  lw $t0, 20($s2)
  bne $t0, $s1, Exit
  addi $s0, $s0, 1
  j Loop
  Exit:

## Slide 14: Any Question ?